## Slide 1
VLSI Implementation of CORDIC Architecture
This project is done under the guidance of Mr.Irfan Ali Sir & Mr.Shyam Sir
by
N150404 N150421 N150428 N150435 N150620

## Slide 2
CORDIC COordinate Rotation DIgital Computer

## Slide 3
Mathematical Formulas:

## Slide 4
The above functions can be implemented by taylor series with some approximations.It includes multiplication of x with x.
1011*1011=
-----------------------------------------
1011
1011+
0000+
1011+
-----------------------------------------
1111001

## Slide 5
A simple multiplication needs many adders,which in turn increase hardware.
We want a multiplierless hardware with greater speed and lower
power consumption.

## Slide 6
How is this possible?

## Slide 7
calculator using cordic algorithm

## Slide 8
Cordic Algorithm was proposed by Volder in 1959.It is improved by Walther in 1971.
It is widely used hardware efficient iterative algorithm for computation of elementary functions such as hyperbolic,arithematic,trigonometric,exponential, logorithmic functions.

## Slide 9
Basic concept of this algorithm is
* To decompose the desired rotation angle into sum of set of predefined elementary rotation angles(lookup table).
*Such that rotation through each of them can be accomplished
with simple shift and add operations,which reduces hardware cost.
For this Cordic algoritm we require only
*3 adders
*1 look up table (register to store predefined values)
*2 shift registers

## Slide 10
Cordic algorithm generally works by rotating the coordinate system through a constant set of angles until the angle is reduced to zero.
For example,to track 60 degrees
60=45+26.6-14+7 These are predefined angles( )
when ,it tracks the angle 60 degrees.

## Slide 11
= 60-45=15 (+ve)
= 15-26.6=-11 (-ve)
=-11+14=3 (+ve
= .
=.
till to track required angle

## Slide 12
Where is the scaling factor to reduce the equation

## Slide 13
Then

## Slide 14
For n iterations,

## Slide 15
Then we take

## Slide 16
LOOK UP TABLE:
i | 
0 | 45
1 | 26.6
2 | 14
3 | 7.1
4 | 3.6
5 | 1.8
6 | 0.9
7 | 0.4
8 | 0.2
9 | 0.1

## Slide 18
i | d_i | α_i | z_i | x_i | y_i
0 | +1 | 45 | 60 | 0.6073 | 0
1 | +1 | 26.6 | 15 | 0.6073 | 0.6073
2 | -1 | 14 | -11.6 | 0.30365 | 0.91095
3 | +1 | 7.1 | 2.4 | 0.53138 | 0.835037
4 | -1 | 3.6 | -4.7 | 0.427 | 0.901459
5 | -1 | 1.8 | -1.1 | 0.4833 | 0.87477
6 | +1 | 0.9 | 0.7 | 0.51063 | 0.8588
7 | +1 | 0.4 | 0.3 | 0.5039 | 0.86677
8 | +1 | 0.2 | 0.1 | 0.4971 | 0.87071
9 |  | 0.1 | 0 | 0.4997 | 0.8661

## Slide 19
ARCHITECTURE OF CORDIC ALGORITHM

## Slide 21: Vectoring Mode:
you have seen 'Rotation Mode' based on the rotation of angle zi .
Now in Vectoring mode according to the position vector of point (xi,yi)
we accumulate angle in zi this is the basic funda of this mode.
Equations:
xi+1=xi-di.yi.2-i
yi+1=yi+di.xi.2-i
zi+1=zi-di.ai ;ai is ith elementary angle
Note that here ;di =-sign(yi)

## Slide 22
Now let us find tan-1(1/3) to know how vectoring mode works
xi+1=xi-di.yi.2-i | yi+1=yi+di.xi.2-i | zi=zi-di.ai | di=-sign(yi)
3 | 1 | 0 | -1
4 | -2 | 450 | 1
5 | 0 | 450-26.565 = 18.4349 | -
2
1
0
y
x
(3,1)
(4,-2)
(5,0)

## Slide 23
Cordic Algorithm
Circular
Coordiniate system
Rotation Mode:
sin(θ),cos(θ)
Vectoring Mode:
tan-1(x),
Linear Coordinate
system
Rotation Mode:
x.z
Vectoring Mode:
y/x
Hyperbolic
Coordiniate system
Rotation Mode:
sinh(θ),cosh(θ)
Vectoring Mode:
tanh-1(x),

## Slide 24
Cordic
x
y
z
Cordic
x
y
z
kn[x.cos(z)-y.sin(z)]
kn[x.sin(z)+y.cos(z)]
0
sqrt(x2+y2)
Circular Co-ordinate System:
In Rotation Mode: In Vectoring Mode:
0

## Slide 25
Cordic
x
y
z
Cordic
x
y
z
x
y+(x.z)
0
x
Linear Co-ordinate System:
In Rotation Mode: In Vectoring Mode:
0

## Slide 26
Cordic
x
y
z
Cordic
x
y
z
kn[x.cosh(z)-y.sinh(z)]
kn[x.sinh(z)+y.cosh(z)]
0
sqrt(x2-y2)
Hyperbolic Co-ordinate System:
In Rotation Mode: In Vectoring Mode:
0

## Slide 27: Implementation of other important functions

## Slide 28: Representation of numbers
we are using 32 bit in our program.If bit size increases precision increases.
Scale the values with

## Slide 31: Implementing cos(θ) and sin(θ)
Cordic
x
y
z
kn[x.cos(z)-y.sin(z)]
kn[x.sin(z)+y.cos(z)]
0

## Slide 32: Look up table for cos(θ) and sin(θ) :
i | αᵢ=
0 | 45
1 | 26.6
2 | 14
3 | 7.1
4 | 3.6
5 | 1.8
6 | 0.9
7 | 0.4
8 | 0.2
9 | 0.1

## Slide 33
decimal | binary | hexcode
45 | 00101101000000000000000000000000 | 2d000000
26.6 | 00011010100100001010001111000000 | 1a90a3c0
14 | 00001110000010010011011101001011 | 0e09374b
7.1 | 00000111001000000000000000000000 | 07200000
3.6 | 0000001110010011011101001011110 | 039374bc
1.8 | 00000001110010100011110101110000 | 01ca3d70
0.9 | 00000000110110011001100110011001 | 00d99999
0.4 | 00000000011100101011000000100000 | 0072b020
0.2 | 0000000000111001010110000001000 | 00395810
0.1 | 00000000000111001010110000001000 | 001cac08
0.6073 | 10011011011110000000000011 | 09b7800

## Slide 34
Prerequisites:
*Representation of numbers
*generate Loop,genvar,block identifier of generate loop
ex:
genvar i;
generate
for(i=1;i<=width;i=i+1)
begin:xyz
....
....
end
endgenerate
*shifting

## Slide 35: sine and cose code:

## Slide 38: Simulation result:

## Slide 39: coshx and sinhx code:

## Slide 41: simulation result:

## Slide 42
Cordic
x
y
z
Cordic
x
y
z
x
y+(x.z)
0
x
Linear Co-ordinate System
In Rotation Mode: In Vectoring Mode:
0
Multiplication
Put Y=0

## Slide 43
Generalized Cordic defined as
  Xi+1 = Xi -  di Yi 2-i
  Yi+1 = Yi + di Xi 2-i
  Zi+1 = Zi - di Ei
Defining  and Ei gives
   = 1 Circular rotations (basic) Ei = tan-12-i
   = 0 Linear rotations Ei = 2-i
   = -1 Hyperbolic rotations Ei = tanh-12-i
  Xi+1 = Xi
  Yi+1 = Yi + di Xi 2-i
  Zi+1 = Zi - d (2-i )

## Slide 44
Take Yi=0
Take inputs Xin and Zin
Create look up table with 2-i (i=….-2,-1,0,1,2,…..)
  Xi+1 = Xi
  Yi+1 = Yi + di Xi 2-i
  Zi+1 = Zi - d (2-i )

## Slide 45
LOOK UP TABLE
a[i]= 2-i
For i=-4 a[-4]=36'h010000000
For i=-3 a[-3]=36'h008000000,
For i=-2 a[-2]=36'h004000000,
For i=-1 a[-1]=36'h002000000,
For i=0 a[0]=36'h001000000,
For i=1 a[1]=36'h000800000,
For i=2 a[2]=36'h000400000,
For i=3 a[3]=36'h000200000,
For i=4 a[4]=36'h000100000,
For i=5 a[5]=36'h000080000,
For i=6 a[6]=36'h000040000,
For i=7 a[7]=36'h000020000,
For i=8 a[8]=36'h000010000,
For i=9 a[9]=36'h000008000,
For i=10 a[10]=36'h00004000;

## Slide 46
CODE FOR MULTIPLICATION
module multiplication(clk,x_in,z_in,out);
input clk;
input [35:0] x_in,z_in;
output reg [35:0] out;
wire [35:0]a[-4:10];
assign
a[-4]=36'h010000000,//fraction part is 12-bits
a[-3]=36'h008000000,
a[-2]=36'h004000000,
a[-1]=36'h002000000,
a[0]=36'h001000000,
a[1]=36'h000800000,
a[2]=36'h000400000,
a[3]=36'h000200000,
a[4]=36'h000100000,
a[5]=36'h000080000,
a[6]=36'h000040000,
a[7]=36'h000020000,
a[8]=36'h000010000,
a[9]=36'h000008000,
a[10]=36'h00004000;

## Slide 47
reg [35:0] y [-4:7];
reg [35:0] z [-4:7];
always @(posedge clk)
begin
y[-4]<=0;
z[-4]<=z_in;
end
genvar i;
generate
for(i=-4;i<=7;i=i+1)
begin:yz
wire z_sign;
wire [35:0] x_shr;
assign z_sign =z[i][35];
if(i[31]==1)
begin
assign x_shr=x_in<<-i;
end
else
begin
assign x_shr=x_in>>i;
end
  Xi+1 = Xi
  Yi+1 = Yi + di Xi 2-i
  Zi+1 = Zi - d (2-i )

## Slide 48
always @(posedge clk)
begin
y[i+1]=z_sign ? y[i]-x_shr :y[i]+x_shr;
z[i+1]=z_sign ? z[i]+a[i] :z[i]-a[i];
if(z[i]==0)
out=y[i];
end
end
endgenerate
endmodule
  Xi+1 = Xi
  Yi+1 = Yi + di Xi 2-i
  Zi+1 = Zi - d (2-i )

## Slide 49: Multiplication Inputs: xin=fa800000 (-5.5) yin=0 zin=02000000 (2)

## Slide 50: Output of multiplication

## Slide 51: Output of division

## Slide 52
module factorial(clk,f,out);
input clk;
input [35:0] f;
output reg [35:0] out;
reg [35:0] a [10:1];
reg [35:0] x [10:1];
wire [35:0] y [10:1];
always @(posedge clk)
begin
a[1]=f-36'h001000000;
x[1]=f;
end
genvar i;
generate
for(i=1;i<=10;i=i+1)
begin:xyz
multiplication u2(clk,x[i],a[i],y[i]);
CODE FOR FACTORIAL

## Slide 53
always @(posedge clk)
begin
x[i+1]=y[i];
a[i+1]=a[i]-36'h001000000;
if(a[i]==0)
begin
if(y[i]==0 )
out=36'h001000000;
else
out=y[i-1];
end
end
end
endgenerate
endmodule

## Slide 54
Uses:
Cordic algorithm used calculations of
Trigonometric functions
Inverse trigonometric functions
square roots
Hyperolic functions
Division and multiplication
Logorithmic functions
Exponential functions

## Slide 55
Applications:
DSP(for MAC blocks)
Image processing
3D Graphics
Robotics
Digital filters
Solving linear systems

## Slide 56: Thank you